## Slide 1
AI SMART WASTE SORTER
Domestic Waste Segregation Using Artificial Intelligence
Team Project Presentation
Categories:
Biodegradable
And
Non-Biodegradable

## Slide 2
Problem Statement
• In our daily life, we generate different types of waste such as food waste, plastic, paper, metal and other materials. Usually, all this waste is put into the same dustbin, which makes proper waste segregation difficult.
• Separating waste manually can be time-consuming, unhygienic and inconvenient, especially at home. When biodegradable and recyclable waste gets mixed together, recycling and composting become more difficult.
• An AI Smart Waste Sorter can help solve this problem by identifying the type of waste using a camera and AI, and then automatically directing it to the appropriate compartment.
• The main need for this project is to reduce manual effort, improve waste segregation, support recycling, maintain better hygiene and encourage responsible waste management at the household level.

## Slide 3
Objectives
• Identify common household waste using a camera and AI.
• Automatically separate waste into appropriate compartments.
• Use sensors to improve detection and monitoring.
• Measure/record waste quantity for household awareness.
• Send uncertain items to a separate compartment instead of forcing an incorrect classification.

## Slide 4
Proposed Solution
• Camera captures the waste item.
• AI model classifies the item.
• Sensors provide additional information such as moisture, metal presence and weight.
• Controller operates a servo/motor-based sorting mechanism.
• Waste is directed to Biodegradable, Recyclable or Other/Unknown compartments.

## Slide 5
System Block Diagram
CAMERA
↓
AI IMAGE CLASSIFIER
↓
┌────────── SENSOR VERIFICATION ──────────┐
│ Moisture • Metal • Weight • Fill Level │
└─────────────────┬──────────────────────┘
↓
CONTROLLER
↓
SERVO / MOTOR
↓
BIODEGRADABLE | NON-BIODEGRADABLE

## Slide 6
Hardware Components
Component | Function
🧠 Raspberry Pi / ESP32 | Main controller; processes data and controls the system
📷 Camera (Pi Camera / ESP32-CAM) | Captures images of waste for AI identification
⚙️ Servo Motor | Moves the flap to direct waste into the correct compartment
📏 Ultrasonic Sensor | Detects waste and measures the fill level of the bin
💧 Moisture Sensor | Helps identify wet/organic waste
🧲 Inductive Proximity Sensor | Detects metallic waste
⚖️ Load Cell + HX711 | Measures the weight of waste
🔔 Buzzer / LED | Provides alerts and system-status indication
🗑️ Multi-compartment Bin | Separates biodegradable, recyclable and other waste
🔌 Power Supply | Provides power to the controller, sensors and motors
🔗 Jumper Wires & Breadboard/PCB | Connects the electronic components
🛠️ Frame / Conveyor / Sorting Flap | Provides the physical mechanism for moving and sorting waste

## Slide 7
Software & AI
• Python can be used for the AI and control logic.
• Computer vision processes the camera image.
• An image-classification model is trained on common domestic waste.
• Example classes: food/organic, paper/cardboard, plastic, metal and other.
• Confidence threshold: low-confidence items are sent to the Unknown compartment.

## Slide 8
Innovation / USP
• Designed specifically for domestic use.
• Multi-sensor verification instead of relying only on the camera.
• Composing Alert .
• Optional waste-weight and fill-level monitoring.
• Can generate a household waste report for awareness.
• Future versions can learn from corrected classifications.

## Slide 9: ADVANTAGES
Automatic waste segregation – Separates waste without manual sorting.
Saves time and effort – Reduces the need for household members to sort waste.
Improves hygiene – Minimizes direct contact with dirty or wet waste.
Better recycling – Helps keep recyclable materials separate from organic waste.
Reduces human errors – AI can identify waste based on trained images and sensor data.
Domestic-friendly – Can be designed in a compact size for home kitchens.
Waste monitoring – Weight and fill-level sensors can track how much waste is generated.
Reduces contamination – Keeping different waste streams separate can improve the quality of recycling/organic processing.

## Slide 10: LIMITATIONS
High initial cost – Camera, AI processor, sensors and motors can make it more expensive than a normal dustbin.
Limited AI accuracy – The system may incorrectly classify unfamiliar or visually similar items.
Mixed waste is difficult – An item containing multiple materials can be difficult to categorize.
Dirty or wet waste – Food residue, moisture and dirt can affect camera/sensor readings.
Maintenance required – Sensors, camera and mechanical parts need regular cleaning and maintenance.
Power requirement – The system needs a continuous power supply or rechargeable battery.
Mechanical blockage – Irregular, oversized or tangled waste may jam the sorting mechanism.
Training data dependency – AI performance depends on the quality and variety of images used for training.

## Slide 11
Working Example
1. User puts a waste item into the input area.
2. Camera captures its image.
3. AI predicts the waste category.
4. Sensors provide supporting information.
5. Controller selects the correct direction.
6. Servo/motor moves the flap.
7. Item falls into the selected compartment.
8. Weight/fill-level data can be recorded.

## Slide 12: Reasons for slow growth of AI-WASTE-SORTER
High cost – Camera, AI hardware, sensors, motors, and maintenance increase the cost compared with a normal dustbin.
Identification is difficult – Some waste looks similar. For example, a dirty plastic container may be difficult for AI to classify correctly.
Mixed/dirty waste – Food residue, water, or multiple materials in one item can reduce classification accuracy.
Different waste categories – Household waste varies from home to home, so one AI model may not work perfectly everywhere.
Mechanical problems – The sorting mechanism can get blocked or damaged by irregularly shaped or wet waste.
Power and maintenance – Sensors, cameras, motors, and controllers require electricity and occasional cleaning/maintenance.
Human behavior – People may still need to place waste properly or remove large/unsafe objects.

## Slide 13
Some indirect uses of AI Smart waste sorter
1. Reduction in fertilizer imports
• The sorter separates biodegradable kitchen waste from plastic and other waste.
• Organic waste can be sent for composting or other organic-waste processing.
• The resulting compost can provide nutrients and organic matter for soil.
---Flow: Kitchen waste → AI sorting → Organic waste → Compost → Soil nutrients → Reduced fertilizer requirement
2. Reduction in CNG requirement
• Properly separated organic waste can be processed through anaerobic digestion.
• This produces biogas, which can be upgraded to biomethane.
• Biomethane can be used as a gaseous fuel and, after appropriate upgrading and compression, can serve applications similar to CNG.
---Flow: Organic waste → AI sorting → Anaerobic digestion → Biogas → Upgraded biomethane → Vehicle/energy fuel
3. More biogas production
• The biggest advantage of segregation is keeping plastic, metal and other contaminants out of organic waste.
• Cleaner organic feedstock is more suitable for anaerobic digestion, making the waste stream more useful for biogas production.

## Slide 14
Conclusion
• AI can assist households in separating common waste automatically.
• The proposed system combines computer vision, sensors and an automatic mechanism.
• The main focus is a practical, low-cost domestic prototype.
• Goal: identify → verify → sort → monitor household waste.

## Slide 15: THANK YOU